## Slide 1
Problems & Solutions for Large-Scale Models
Andrew Rohne
March 15, 2019

## Slide 2: Introduction
Based on TRB Session
Eight Presentations

## Slide 3
New ideas for demand estimation: Can we characterize travelers and locations based on movement traces?

## Slide 4: Methodology
Clean Data (a year of cellphone data)
Identify attributes
  Time between points, if device is moving
  Start and end locations with DBSCAN algorithm
Identify trips
Characterize Travelers
  K-medoids approach
Background: gravity model inadequate

## Slide 5: DBSCAN
Density-Based Spatial Clustering of Applications with Noise
Groups points with a lot of neighbors
  GPS Trace Data – ATRI, GPS Household Survey
Unsupervised Algorithm

## Slide 6: DBSCAN Example

## Slide 7: DBSCAN Example

## Slide 8: K-medoids
Unsupervised Algorithm for Clustering Data
  Similar to k-means clustering
  Not really meant for spatial data
User provides number of centers
Algorithm returns medoids
  Medoids ~~ Centroids (“Median Centroids”)
  Actual datapoints as centers
All points assigned a Medoid

## Slide 9: K-medoids Example - Medoids

## Slide 10: K-medoids Assigned Clusters (k = 2)

## Slide 11: K-medoids Assigned Clusters (k = 3)

## Slide 12: K-medoids Assigned Clusters (k = 4)

## Slide 13: K-medoids Assigned Clusters (k = 4)

## Slide 14: Traveler Clusters

## Slide 15
Synthesizing Household and Person-Level Attributes Jointly for Individual Geographies Using Hidden Markov Model

## Slide 16: Methodology
Uses HMM to perform multi-level (person and household) synthesis
HMM = Hidden Markov Model

## Slide 17: Hidden Markov Model
Markov Process with Unobserved States
Markov Process
Selection depends on prior state

## Slide 18: Case Study 1

## Slide 19: Case Study 2

## Slide 20
Synthesizing Household and Person-Level Attributes Jointly for Individual Geographies Using Hidden Markov Model

## Slide 21: Methodology
Uses Response Surface Methodology to iteratively adjust parameters
Response Surface Methodology:
A sequence of designed experiments to obtain an optimal response1
1: Wikipedia, https://en.wikipedia.org/wiki/Response_surface_methodology, accessed 3/12/19

## Slide 22: Methodology – Model Structure
TPMS calibration
Parameter adjustments
Calculating non-dominated adjusting solutions
Selecting some non-dominated adjusting solutions
Doing RSM experiment
Parameters evaluation
Selecting the candidate parameters
Choosing the deviation range
Evaluating the parameters
TPMS validation
Adjustment solution selection
Evaluating the validity of each adjusting solution
Choosing the best adjusting solution
Evaluating the non-dominated adjusting solutions
Proposed model structure for the calibration process
Notes: In the TPMS calibration stage, the objective is to find a set of non-dominated solutions that can improve reproduction of the base-year statistics.
In the TPMS validation stage, the best fitted solution, in terms of reproducing the base year and validity, that at the same time is superior in term of model system’s prediction capabilities. can be obtained.

## Slide 23
Pairing Discrete Mode Choice Models and Agent-Based Transport Simulation with MATSim

## Slide 24: Methodology
Simulate Mode Choice
Score Against Data
Re-plan Mode Choice

## Slide 25: Methodology

## Slide 26
TRB 2019, 16 January 2019
“Car cannot be used if it has not been moved to the current location.”
”Additionally, the car must arrive back at home.”
Case Study: Zurich

## Slide 27
TRB 2019, 16 January 2019
“I may need a car later on, although not on the first trip.”
Case Study: Zurich

## Slide 28
Bayesian Optimization for Transportation Simulators

## Slide 29: Bayesian Optimization
Design Strategy for global optimization
  Strategy…
  Global Optimization: attempt to find the global minima or maxima

## Slide 30: Bayesian Optimization Strategy
Objective Function (function to maximize or minimize) Unknown
Treat it as random + prior (probability distribution based on beliefs)
Function evaluations treated as data
Prior updated to form posterior distribution
Posterior distribution determines next query point

## Slide 31: Global Maxima/Minima

## Slide 32
Microscopic Travel Demand Modeling: Using the Agility of Agent-Based Modeling W/o the Complexity of ABMs

## Slide 33: MITO Model
Agent-Based
Trip-Based
Accounts for travel time budgets
(and it’s open source)

## Slide 34: MITO Model Design

## Slide 35: MITO Case Study

## Slide 36
Model Averaging: Revisiting Our Approach to Decision Rule Heterogeneity and Improving Our Travel Behavior Models

## Slide 37: Background
Random Utility Model vs. Random Regret Minimization vs. Decision Field Theory
Random Utility Model: “normal” models
  Utility towards alternative varies across individuals
  Utility randomness assumed normal
Random Regret Minimization models
  Individuals’ urge to minimize regret after choice
Decision Field Theory
  Preferences for alternatives update over time

## Slide 38: Methodology
Estimated Models (RUM, RRN, DFT)
Weighted candidate models
  Based on performance, e.g. Log-likelihood
  Average Models
Provided better fit over one model

## Slide 39
Calibrating Activity-Based Travel Demand Model Systems via Microsimulation

## Slide 40: Methodology

## Slide 41: Methodology

## Slide 42: Case Study

## Slide 43
www.rsginc.com
Contacts
Andrew Rohne
Senior Consultant
andrew.rohne@rsginc.com
513-314-9901