## Slide 1: CAV Microsimulation – Modeling the Latest Research
March 15, 2019
Rob Bostrom, CDM
Eric Plapper, HDR

## Slide 2: Presentation Summary
ODOT Project Overview
CAV Overview
CAV Literature Review
  CAV Penetration Rates
  Impacts of CAV Technologies on Traffic Modeling
  CAV Traffic Simulation
  Literature Review Sources

## Slide 3: Ohio DOT Literature Review Project

## Slide 4: ODOT Lit Review Team
CDM Smith
Caliper
Steve Shladover
HDR
Delft
OSU
Report being reviewed by ODOT

## Slide 5: Work Tasks
Literature Review
  Traffic Simulation SOP
  “Big Picture”
  Simulation tools
    TransModeler
    Vissim
Corridor Studies
  Marysville
  Ohio Turnpike
  Brent Spence Bridge

## Slide 6: Map of Marysville OH – US 33

## Slide 7: Modeling Improvements on Ohio Turnpike

## Slide 8: Brent Spence Bridge Modeling

## Slide 9: Connected and Automated Vehicles (CAV) Overview

## Slide 10: CAV Terminology
Connected Vehicles - wireless communication among vehicles (Vehicle-to-Vehicle or V2V) and/or between the vehicles and the roadway infrastructure (Vehicle-to-Infrastructure or V2I)
Automated Vehicles - vehicles with varying combinations of human and machine decision making and control
CAV - V2V and V2I vehicles with automated functions
Technological evolution – Collision avoidance, cooperative adaptive cruise control, lane detection, dynamic route guidance, on-board ranging, mapping, traffic jam warning
SAE levels of automation – driver assist features available today through semi-automated, then driverless vehicles

## Slide 11: CV Technology

## Slide 12: AV Technology

## Slide 13: Levels of Automation

## Slide 14: Example Capabilities
Autonomous Vehicle Capabilities | Connected Vehicle Capabilities | Combined Capabilities
Advanced Lane Detection | Dynamic Route Guidance | Modular Lanes
Adaptive Cruise Control with Steering Assist | V2V Basic Safety Messages | Cooperative Adaptive Cruise Control
Automated Emergency Braking | Queue Warning | Speed Harmonization

## Slide 15: A Future with CAVs
CAVs have the potential to be disruptive and transformational.
When will it all happen?
What will the impacts be?
How will driverless cars change the way we travel?
CDM Smith’s Ed Regan speculates
https://www.youtube.com/watch?v=bBcsnbq-7Ic

## Slide 16: CAV Status in 2019
More than 17 shared AV pilots in 8 states underway
Supervision of safety “driver”
Transformational technological developments take time
  Laptop computers
  Cell phones
Planning community needs procedures and methods to address both potentially positive and potentially negative outcomes
Updates to modeling and forecasting tools that will be necessary to account for CAVs
Updating Regional Transportation Planning and Modeling Tools
to Address Impacts of Connected and Automated Vehicles
  Vol 1: Executive Summary http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_rpt_896v1.pdf
  Volume 2: Guidance http://nap.edu/25332

## Slide 17: CAV Penetration Rates

## Slide 18: Uncertainty of CAV Penetration Rate
Uncertainties related to penetration rates
  Pace of technological maturity
  Rate of inclusion of technology in new vehicles and retirement of old vehicles
  Extent of use of technology by consumers
CAVs have the potential to be disruptive and transformational.
These uncertainties are ripe for scenario planning and further microsimulation analysis

## Slide 19: AV Adoption Rates
Source: HDR

## Slide 20: Long Implementation Time is Likely
Private ownership likely to continue, decreasing interest in shared AVs
VMT will probably increase with AVs
AV penetration may be slowed by political and regulatory issues
Accidents may slow evolution of AV technology
Until field tests or initial deployments can actually measure impacts, modeling of traffic impacts should continue

## Slide 21: Penetration Rate Example
Click to add text
Source: Iowa DOT and HDR, Interstate 80 Planning Study June 2017

## Slide 22: Penetration Rate Example
Source: Amitai Bin-Nun, Alex Adams, and Jeffrey Gerlach (2018)
America’s Workforce and the Self-Driving Future:
Realizing Productivity Gains and Spurring Economic Growth

## Slide 23: Candidate CAV Scenarios – Another Example

## Slide 24: Refining and Using CAV Scenarios
Involve stakeholders in review and detailed definitions of scenarios
Include demographic parameters to help define plausible futures, e.g.
  Population changes
  Residential and land use changes
  Regional economics and job locations
Define measures to use in analyzing scenarios, e.g.
  Vehicle Miles Traveled (VMT)
  Vehicle Hours Traveled (VHT)
  Cost of transportation
  Equity impacts
Use simulation models such as Vissim and TransModeler

## Slide 25: Impacts of CAV Technologies on Traffic Modeling

## Slide 26: Impacts of CAV on Traffic Operations
Transportation cost
Transportation safety
Vehicle operations (including capacity changes, congestion, and other traffic impacts)
Energy use and related emissions
Personal mobility and convenience (including shared, owned, or rented vehicles)

## Slide 27: AV impacts reflected in travel model
Source: Vovsha and Vyas wsp Dec 2018

## Slide 28: Simulated Highway Capacity Improvement
Source: (Liu, Kan, Shladover, Lu, & Ferlis, 2018)

## Slide 29: AO45 Capacity Factors vs Penetration Rate
Source: Vovsha and Vyas wsp Dec 2018

## Slide 30: Framework for CAV Planning and Modeling
Source: Updating Regional Transportation Planning and Modeling Tools
to Address Impacts of Connected and Automated Vehicles NCHRP 896 Vol 1 2018

## Slide 31: CAV Impacts on Modeling
Modeling in the Past:
  Travel behavior and mode choice trends for next 20-30 years relatively stable
  Model calibration calibrated w survey data and validated with existing mode usage
With CAVs: Not any more
  New modes
  different behavior
  different impacts
Going forward: models need to be adjusted

## Slide 32: CAV Traffic Simulation

## Slide 33: Societal Trends Driving Uncertainty
Changing Demographics
Improved Technology
Shifting User Preferences
Improved Travel Options
Millennial travel behavior
Automated vehicles
Urbanization
Better walking and biking options
Aging population
Generation Z
Workplace automation
Improved user information & navigation
Smart City
Shift from individual ownership to fleet ownership
Telecommuting
E-commerce & delivery options
Improved public transit
Shared mobility
EVs
Notes: Supply: Transportation more readily available through AV/CV mobility improvements, ride hailing, car sharing, trip integration across modes
Demand: number of trips and types of trips are changing due to changing demographics, user preferences

## Slide 34: Incorporating Uncertainty into Travel Modeling
Demand Side
Modify demand to reflect AV adoption rates on usage
Supply Side
Modify supply side to reflect AV adoption on capacity
Change “When” and “How” People Travel
Change “What Happens” on the Road
When People Travel

## Slide 35: Traffic Simulation of CAVs
Two Key Simulation Models Used with CAVs
Vissim – Some adjustments to internal parameters and Car Following made. Used in numerous CAVs-related research studies.
  Stanek, D., R. T. Milam, E. Huang, et. al. Measuring Autonomous Vehicle Impacts on Congested Networks Using Simulation. Fehr & Peers, 2018.
TransModeler – allows new vehicle classes equivalent to SAE levels. Used with adjustments documented in FHWA study
  Stabler, B., M. Bradley, D. Morgan, H. Slavin, and K. Haque. Volume 2: Model Impacts of Connected and Autonomous/Automated Vehicles (CAVs) and Ride-Hailing with Activity-Based Model (ABM) and Dynamic Traffic Assignment (DTA) – An Experiment FHWA, 2018.

## Slide 36: Florida DOT TransFuture: Inputs
Notes: Output displays probabilistic results and confidence intervals for factors such as annual average daily traffic (AADT) and vehicle miles traveled (VMT).
In this case we are viewing impacts on congestion and crashes

## Slide 37: Florida DOT TransFuture: Outputs
Notes: Output displays probabilistic results and confidence intervals for factors such as annual average daily traffic (AADT) and vehicle miles traveled (VMT).
In this case we are viewing impacts on congestion and crashes

## Slide 38: Florida DOT TransFuture: Business as Usual
8 lane by 2045;
10 lane by 2056
6-lane capacity
8-lane capacity
10-lane capacity
Notes: Florida highway corridor with travel demand by year
Capacity of 6, 8, 10 lane corridors
Projected to need to grow to 8 lanes by 2045 and 10 lanes by 2056

## Slide 39: Florida DOT TransFuture: with CAV technology
Notes: Demand increases based population growth, demographics, shifting user preferences
Capacity also increases based on AV/CV technology
6 lane highway is meeting demand in 2045, compared to baseline showing need for 8 lane capacity in 2045, 10 lane capacity in 2056

## Slide 40: Incorporating CAVs into Supply Side
  Different rules for merging
  Different rules for passing
  Adherence to speed limits
  Acceleration/deceleration
  Ability to form platoons
  Shorter headways
  Speed harmonization
  Remove human element from vehicle control
AV
AV
AV
MV
AV
AV
AV
AV
MV
MV
Changes in Driving Patterns:

## Slide 41: Measuring CAV Impacts
Notes: Safety impacts are also considerable
Around 90% of accidents are caused by human error
Unimproved scenario in year 2040:
  Crashes increase by 9%
  Vehicle crowding increases 55%
  Misery index increases 6-12%
With added lane and AV improvements:
  Crashes decrease by 59%; fatal/major injury crashes decrease by half (with lane addition alone crashes went up 14%)
  Vehicle crowding is down 35%
  Misery index is down -1-3%

## Slide 42: Modeling Risk and Uncertainty in CAVs
Multiple Scenarios are needed to analyze uncertainty
Two analysis methodologies for uncertainty
  Scenario Planning
  Exploratory Modeling and Analysis
Simulation modeling interfaces useful
  e.g. integrated dynamic traffic assignment (DTA) model and activity-based model (ABM) with TransModeler in FWHA study

## Slide 43: Key Literature Sources

## Slide 44: CAV Literature Review for ODOT
Source: CDM Smith
Notes: What is important in this spreadsheet are the various tabs including impacts and modeling – shown along the bottom, and the inclusion of an abstract and some key work columns to provide high level overviews of documents. Most included links to the documents.

## Slide 45: Some CAV Research Reviewed
Updating Regional Transportation Planning and Modeling Tools to Address Impacts of Connected and Automated Vehicles, Volumes 1 and 2 Zmud et al, NCHRP Report 896 2018).
Connected and Automated Vehicle Concept Dimensions and Examples Shladover and Greenblatt Ucal Berkley for USDOE 2018
The Future of Autonomous Vehicles: Lessons from the Literature on Technology Adoption UCal Berkley for Caltrans 2018
Autonomous Vehicle Implementation Predictions Todd Litman Victoria Transport Policy Institute 2018
An Assessment of Autonomous Vehicles: Traffic Impacts and Infrastructure Needs Kockelman et al Univ of Texas Austin 2017
Autonomous Vehicles and Connected Vehicle Systems: Flow and Operations Considerations Mahmassani for Transportation Science 2016
Notes: NCHRP 896 provides an excellent overview of the modeling issues associated with CAVs and the kinds of changes that are needed in the different types of models. Particularly the executive summary is a good place to start in understanding modeling of CAVs.
Shladover and Greenblatt do a nice job of describing CV and AV technologies and business models.
The Lessons about Technology Adoption looks at the introduction of the electrical grid, automobiles, and computing capability and the decades long adoption period and what that might mean for CAVs.
Litman provides a good overview of predicted costs, benefits, and impacts of CAVs, both private and shared. He has a number of useful tables and graphics to illustrate the impacts.
Kockelman is a noted researcher in Texas. Her Impacts and infrastructure report uses public survey information, including willingness to pay, to help predict CAV adoption. Report includes useful discussion of the impacts and relative cost of different AV technologies on the roadway infrastructure.
Mahmassani was invited to submit his paper on CAVs for the 50th anniversary issue of Transportation Science. He simulated flow control of Avs to estimate impacts.

## Slide 46: Some CAV Research Reviewed - 2
Model Impacts of Connected and Autonomous/Automated Vehicles (CAVs) and Ride-Hailing with an Activity-Based Model (ABM) and Dynamic Traffic Assignment (DTA)—An Experiment Volume 2 FHWAHEP Report 18081 Stabler, Bradley, Morgan et al April 2018
Predicting the adoption of connected autonomous vehicles: A new approach based on the theory of diffusion of innovations Talebian and Mishra, University of Memphis (2018)
Preparing for the Future of Transportation: Automated Vehicles 3.0 USDOT Oct 2018
America’s Workforce and the Self-Driving Future: Realizing Productivity Gains and Spurring Economic Growth Amitai Bin-Nun, Alex Adams, and Jeffrey Gerlach Securing America’s Energy Future June 2018
Scenario Modeling and EMA for CAVs Vince Bernardin RSG Sep 2018
Modeling impacts of Cooperative Adaptive Cruise Control on mixed traffic flow in multi-lane freeway facilities. Transportation Research Part C: Emerging Technologies, 95 Liu, Kan, Shladover et al December 2017
Notes: The Model Impacts report for FHWA used Exploratory Modeling Analysis to analyze many scenarios and integrated travel demand models with TransModeler to analyze Jacksonville regional data.
The Memphis report used survey techniques to examine how AVs might be implemented.
AV 3.0 built on AV 2.0 as the USDOT policy for promoting CAVs while assuring public safety without favoring any particular technology approach.
The Workforce study is a favorite of DriveOhio and looks at the impacts of CAVs on transportation industry labor as well as potential redistribution of jobs as a result of different scenarios for AV implementation either as shared use in cities or with private ownership.
Bernardin’s presentation dealt with the EMA work by RSG as well as other studies including scenario planning in Burlington VT. Contained useful graphics.
Shladover’s analysis of CCAC described some adjustments made to Vissim in analyzing the impacts on traffic flow of CAVs at various headways including the use of dedicated lanes.

## Slide 47: TFResource wiki
On line resource created by a group under the Travel Demand Forecasting Committee of the Transportation Research Board. Provides information and insights into needed adaptations of existing transportation planning models http://tfresource.org/Content_Charrette:_Autonomous_Vehicles
Identified potential model changes and improvements; highlighted state applications of models http://tfresource.org/Autonomous_vehicles:_Modeling_frameworks

## Slide 48: Lessons Learned from Literature Search
Unrealistically high expectations by the media amplify the overheated marketing rhetoric of some industry spokespeople.
Highly-publicized accidents raise public skepticism. Gradual rollout and even more gradual market penetration of AVs are expected.
CAV analysis is speculative and uncertain.
To address the uncertainty of CAVs implementation rates define and analyze multiple scenarios

## Slide 49: Lessons Learned from Literature Search -2
Models can be enhanced to handle most CAV uncertainties.
Models cannot tell what will happen but can help understand range of futures and potential policies.
Simulations should be set up so that the market penetration level is an adjustable parameter.
Vissim modifications to model the impacts of CAVs as identified by PTV should be implemented and used. Add TNC mode and zero occupancy vehicles.
TransModeler adjustments as documented in FHWA report should be reviewed and built upon.

## Slide 50: Remaining Tasks for ODOT
Review/finalizing document
Updating literature sources
Starting corridor studies
  Marysville
  Ohio Turnpike
  Brent Spence Bridge

## Slide 51: Contact Information
Rob Bostrom, CDM Smith
Bostromnr@cdmsmith.com
direct: 859.244.8882
mobile: 859.312.2232
Eric Plapper, HDR Inc.
Eric.Plapper@hdrinc.com
QUESTIONS?